## Slide 1
LabAIAgent · technical briefing
1
LabAIAgent
The universal AI-agent gateway for laboratory instruments
Vendor-neutral control · six fail-closed safety layers · a tamper-evident audit trail —
one instrument at a time, for every agent runtime you already use.
v1.4.1
Apache-2.0
232 tests · 4 review rounds
20 fixed tools
MCP · OpenAI · REST · 5 frameworks
stdlib-only core
RS-232 · TCP · HTTP/REST · watched-folder exports · Windows COM · SiLA 2
If your instrument can talk at all, an agent can drive it — safely, and on the record.
Notes: Positioning: LabAIAgent is the safety and audit layer that lets ANY AI agent operate real lab instruments. Open with the one-liner, then the chips: open source, evidence-heavy, framework-neutral.

## Slide 2
Why agent-driven labs fail
Four engineering facts. Ignore any one of them and the failure mode is predictable.
LabAIAgent · technical briefing
2
Physical actions are not idempotent
A tool call can be retried; an aspirate cannot be un-aspirated. The cost of a false negative in a safety check is unbounded — so every check must fail closed.
Instruments speak six protocols
A 2019 plate reader exports CSV to a folder. A 2010 pump is RS-232. A vendor SDK is Windows COM. REST-only integration covers the minority of a real lab.
Agents speak many protocols too
Claude wants MCP, OpenAI wants a functions array, LangGraph wants BaseTools, your scheduler wants REST. A layer welded to one runtime is obsolete next release.
Instrument N+1 must not touch 1..N
If adding an instrument (or an agent framework) means editing what already works, integration cost grows superlinearly and the project stalls.
LabAIAgent is organised around these four constraints — not around any single vendor, instrument, or model.
Notes: Each card is a failure mode we designed against. Emphasize non-idempotency: retry logic that is fine in software is catastrophic on hardware.

## Slide 3
One gateway. One invocation path. No exceptions.
Every agent runtime renders the same 20 tools; nothing reaches hardware except through LabSession.call.
LabAIAgent · technical briefing
3
Claude / MCP
OpenAI · Gemini
LangChain · LlamaIndex
CrewAI · AutoGen · smol.
REST / OpenAPI
AGENT GATEWAY 20 fixed tools, rendered mechanically per runtime · API keys · roles · per-actor ceilings · async jobs · SSE
LabSession.call — THE single invocation path: safety evaluation → per-device lock → execute → audit
Safety engine 6 layers, fail-closed
Scheduler per-device locking
Audit log HMAC hash-chained
Driver contract — @read / @write / @procedure declared once → validation, manifest, agent reference, every schema
RS-232
TCP
HTTP
filewatch
COM
SiLA 2
Why this shape
One policy point. Ceilings, limits, interlocks, approvals and audit apply to every caller identically — agent, script, or CLI.
Adding instrument N+1 changes no tool schema, in any framework, ever.
Adding agent framework N+1 is a ~100-line shim into the same dispatch.
Core is stdlib + PyYAML: installs on locked-down instrument PCs with no build toolchain.
Notes: Walk top to bottom. The load-bearing claim: there is exactly ONE policy point. Two ways to actuate hardware means one of them is unaudited.

## Slide 4
20 tools. Fixed. For a lab of any size.
An agent choosing among 400 generated tools chooses badly; one given a stable grammar navigates any lab with the same competence.
LabAIAgent · technical briefing
4
20
fixed tools
zero per-instrument schemas
Discovery is data, not schema: list_devices → describe_device returns the instrument's limits, units and operating notes as content the model reads — so hardware changes never invalidate an integration.
Every adapter — MCP, REST, OpenAI, LangChain… — renders THIS registry and calls THIS dispatch.
Discover
list_devices
describe_device
lab_reference
snapshot
Operate
read_state
write_state
run_procedure
run_protocol
Jobs
get_job
list_jobs
cancel_job
Safety & governance
emergency_stop
request_approval
get_audit_log
Knowledge (PubMed-only)
search_literature
list_protocol_templates
instantiate_protocol_
template
Continuity & evidence
lab_tasks
run_records
submit_feedback
Notes: This is the anti-pattern slide: 'one tool per capability' scales the tool list with the lab and breaks every prompt when hardware changes. Our surface is a grammar, not a catalog.

## Slide 5
Meet your agents where they already are
No SDK lock-in: native MCP, native tool schemas, framework shims, or plain HTTP — all onto the same dispatch and safety engine.
LabAIAgent · technical briefing
5
Claude MCP stdio + MCP over HTTP; resources for lab context
OpenAI / Gemini native tool-calling schema exporters
LangChain / LlamaIndex BaseTool / FunctionTool shims
CrewAI / AutoGen / smolagents first-class adapters
Anything with HTTP REST + OpenAPI 3.1 + SSE events
Python LabClient SDK / LabSession embedding
Deployment — the recommended ladder
$ labaiagent serve --lab lab.yaml --readonly # start here
$ labaiagent serve --lab lab.yaml --dry-run # then this
$ labaiagent serve --lab lab.yaml --http \
--auth principals.yaml --tls-cert crt --tls-key key \
--watchdog 15 # only then live
# one port: REST /tools/* · /openapi.json · POST /mcp
# /events (SSE) · / (operator dashboard) · /metrics
Or embed it in Python
from labaiagent import LabSession
s = LabSession.from_config("lab.yaml")
s.connect_all()
s.read("cycler", "block_temperature")
s.write("cycler", "block_temperature",
value=95) # checked, then actuated
s.run("lh", "transfer", source_well="A1",
dest_well="B1", volume=50.0)
Notes: Live demo cue: labaiagent serve --readonly with Claude Desktop takes under a minute. Stress the rollout ladder: readonly, then dry-run, then live.

## Slide 6
Six fail-closed layers: model to motor
Every layer answers 'no' on ambiguity. A refused action is the most important audit record we write.
LabAIAgent · technical briefing
6
1
E-stop latch halts everything; only a named human resets; devices re-self-test before returning
2
State gate no actuation on BUSY / ERROR / quarantined / disconnected instruments
3
Parameter limits unit-aware ranges declared by the driver; config may only NARROW them
4
Interlocks lid closed, plate present, destination free, centrifuge balanced — fail closed if unknown
5
Per-actor ceilings & rate limits each identity has an autonomy ceiling and call budget, enforced in-engine
6
Approval tokens HIGH/CRITICAL actions need a scoped, expiring, single-use human approval (e-signed)
Gated per liquid movement — on real hardware
The Opentrons driver speaks the robot-server's live atomic-command API: load_pipette → pick_up_tip → aspirate → dispense. Volume limits, interlocks, rate limits, approvals and audit apply to every single aspirate — not to an opaque protocol upload.
Retry-safe by construction
Once a physical command is enqueued, nothing retryable can escape — a transient blip can never re-run an aspirate. Adversarially reviewed and regression-tested (REVIEW.md 4.2).
Notes: Key line for robotics engineers: on the Opentrons driver, OUR safety engine gates each individual aspirate over the live command API — not a two-hour protocol blob. And errors after actuation are never retryable (review finding 4.2).

## Slide 7
Security: wire to bench, defense in depth
Networked lab control is treated as what it is — an attack surface in front of moving hardware.
LabAIAgent · technical briefing
7
Transport TLS ≥ 1.2 native; refuses to serve unauthenticated off loopback — that is an incident, not a configuration
Identity API keys hashed at rest, constant-time compare; per-IP brute-force lockout (429 BEFORE any comparison); 4 roles: observer → operator → approver → admin
E-signatures per-person PBKDF2 passwords (200k iterations), re-entered at each approval signing — the key authenticates the connection, the password authenticates the PERSON
Audit authenticity HMAC-SHA256 keyed hash chain: whole-file rewrite without the key is detectable; a broken chain refuses to be extended
Hardened HTTP 2 MiB body cap · Transfer-Encoding rejected (411, anti-smuggling) · nosniff / no-store / no-referrer · SSE subscriber cap · 500-step protocol cap
Agent oversight pre-execution reviewer (rule-based or foundation-model, FAILS CLOSED) · refusal-streak auto-suspension · human-only reinstatement
Reviewed like a target
4
adversarial review rounds, published
31
accepted findings, all fixed
1:1
finding-to-regression-test, enforced
300
randomized examples per property test
Notes: For security engineers: constant-time key compare, lockout BEFORE comparison (no oracle), X-Forwarded-For deliberately untrusted, chunked TE rejected against request smuggling. THREAT_MODEL.md states residual risks honestly.

## Slide 8
Evidence fit for a reviewer — or a regulator
Two integrity-protected artifacts: the append-only audit chain (ground truth) and signed run records (the portable extract).
LabAIAgent · technical briefing
8
Hash-chained audit log (JSONL, fsync'd)
rec 1 prev_hash
HMAC-SHA256
rec 2 prev_hash
HMAC-SHA256
rec 3 prev_hash
HMAC-SHA256
Every invoke, result, REFUSAL, error, approval, e-stop. Edit or delete anything → every later link fails verification. Refusals are recorded on purpose: they are the proof the controls were live.
Signed run record — written for every protocol run (success, failure, or cancel)
{ "body": {
"record_id": "e2e7077ad080493e",
"status": "done", "actor": "agent:claude",
"software": {"labaiagent": "1.4.1", ...},
"devices": [{"id": "lh", "driver_version": ...}],
"protocol": { # AS EXECUTED
"steps": [args, results, errors, ms] },
"audit_slice": { "n_records": 5,
"records": [ ...hashes intact... ] } },
"integrity": {
"sha256": "…", "signature": "HMAC-SHA256…" } }
$ run_records verify → "checksum and signature verify"
Attributable
Legible
Contemporaneous
Original
Accurate
+ Complete · Consistent · Enduring · Available
ALCOA+ by construction — the substrate 21 CFR Part 11 expects (mapping: docs/COMPLIANCE.md).
Reproducibility, operationalised: a colleague reconstructs the run from one file — no database join, no log archaeology.
Notes: ALCOA+ is the data-integrity vocabulary QA people use. The run record is what a methods section cites: protocol as executed, driver versions, actor, audit slice — one self-contained, verifiable file.

## Slide 9
Remembers. Recovers. Humans stay in charge.
Durable memory (SQLite beside the audit log): task board, incidents, quarantines, checkpoints — all survive restarts.
LabAIAgent · technical briefing
9
Human records tasks priority + optional protocol; approver-only
Agent executes run_protocol(task_id) checkpoints every step to disk
CRASH power loss mid-run — in-memory state gone
Restart remembers startup report: interrupted tasks, open incidents, quarantines
Resume, not restart resume=true skips completed steps; $context restored
Fault → intelligence PhysicalError ⇒ quarantine + incident + diagnosis from the driver's own notes
Human closes the loop named resolve_incident lifts the quarantine; work continues
What the agent gets instead of a stack trace
error: PhysicalError:
source well H12 is EMPTY
incident: inc_91ab opened
device lh: QUARANTINED
diagnosis:
1. Do NOT retry the failed
call — physical faults do
not clear by repetition
2. Verify the well map vs.
the physical plate
3. Driver notes: tips <10 uL
unreliable; check volumes
resolve: HUMAN ONLY
Overnight autonomy needs exactly this: nothing forgotten, nothing blindly retried, nothing un-quarantined without a named human.
Notes: Narrate as the overnight story: power loss at 2am. On restart the server prints exactly where it stopped; resume skips completed steps; a physical fault quarantines the instrument with a diagnosis instead of a stack trace. Demo: examples/06 and 07.

## Slide 10
Built to be operated, not just demoed
Operator console, Prometheus metrics, heartbeat watchdog, and opt-in parallel execution — the unglamorous layer that makes it deployable.
LabAIAgent · technical briefing
10
● ● ●
LabAIAgent — operator console GET / (self-contained HTML, zero CDN)
12
instruments
9
idle
2
busy
1
error
clear
e-stop
lh — Opentrons Flex
BUSY
reader — SpectraStar
IDLE
cycler — ProFlex
IDLE
pump_2 — Acme P-200
ERROR · quarantined
E-STOP
live events (SSE): job.progress · device.heartbeat_lost · approval.issued · record.written
GET /metrics
Prometheus text format: devices by state, e-stop latch, jobs, tasks, incidents, quarantines, audit head — for the Grafana/Alertmanager stack you already run
--watchdog 15
probes each idle instrument's own self-test; 3 strikes → ERROR (actuation refused) + event; auto-recovers ONLY what it tripped; never probes mid-actuation, never overrides quarantine
parallel=true
DAG waves grouped BY DEVICE: instruments overlap, same-device order stays strict, per-call safety unchanged; abort/cancel honoured inside every lane
Notes: The dashboard is one self-contained HTML page served at / — no build step, renders on an air-gapped network, and it has NO privileged path: it calls the same authenticated tool endpoints agents do.

## Slide 11
A defensible compliance story — with the gaps stated
We ship the technical controls and the paperwork skeleton; your QA executes and owns the validation. No compliance theater.
LabAIAgent · technical briefing
11
Shipped technical controls → 21 CFR Part 11
§11.10(a)
validation — 232 automated tests + executable IQ/OQ/PQ template
§11.10(c,e)
protected, time-stamped, append-only audit trail (keyed chain)
§11.10(d,g)
access control: hashed keys, lockout, 4-role authority checks
§11.10(f,h)
operational sequencing (safety engine) + device checks (self-test, watchdog, verified writes)
§11.50/70
signatures embedded in the chain — not excisable
§11.200/300
two-component signing: key + per-signing PBKDF2 password; failures audited
What your QA still owns (we say so)
SOPs, training, signature accountability (§11.10 i–k)
Executing the validation on YOUR instruments
Key/password lifecycle and record retention
docs/VALIDATION_PLAN.md
A fill-in IQ/OQ/PQ: 7 installation checks, 11 operational checks per instrument (incl. fault injection, kill-and-resume, watchdog unplug), 5 performance checks per assay. The system generates its own evidence — every row cites an audit range or a signed run record.
GAMP 5: category-4 configured product; risk classes (NONE→CRITICAL) are first-class in the framework itself.
Notes: This slide wins trust by NOT overclaiming. Part 11 compliance is a property of a validated deployment; we make every clause traceable to a control and hand over the IQ/OQ/PQ to execute.

## Slide 12
Engineering rigor you can audit, not admire
Every claim in this deck is falsifiable from the repo: run the suite, read the review record, execute the release gates.
LabAIAgent · technical briefing
12
232
tests, run 3× per release (zero-flake gate)
0
ruff + mypy findings across 58 typed modules
4
adversarial review rounds, published in REVIEW.md
7
runnable end-to-end examples
Chart: Test suite growth by release
| v1.2.0 | v1.3.0 | v1.4.0 | v1.4.1
tests | 181 | 196 | 218 | 232
Run like a product, not a repo
Property-based testing (Hypothesis) on the safety validator, unit algebra, and audit-chain mutation detection
Every accepted review finding ships with a named regression test — 1:1, enforced
G1–G7 release gates (docs/RELEASE_PROCESS.md): triple-run flake gate, clean-venv install, security regression, review-debt zero
Safety-path changes need two reviews — one adversarial, documented (CONTRIBUTING.md)
SemVer where safety may tighten in a MINOR but never loosens outside a MAJOR (SUPPORT.md)
Notes: The chart shows test growth per release. Round 4 was an independent adversarial review of our own new code that found 12 real defects (2 critical) — and we published them. That transparency IS the sales pitch to engineers.

## Slide 13
Instrument N+1: an afternoon, not a quarter
Describe the instrument once, declaratively. Validation, manifest, agent reference, and every framework schema are derived.
LabAIAgent · technical briefing
13
A complete driver — the declaration IS the integration
class AcmePump(Device):
vendor, model, category = "Acme", "P-200", "pump"
notes = "Silently rejects setpoints while priming —"
"the driver drains SYST:ERR? to catch it."
def _connect(self): self.link = open_serial(...)
def _halt(self): self.link.write("STOP")
@read("flow_rate", unit="uL/s")
def get_flow(self) -> float: ...
@write("flow_rate", risk=Risk.MEDIUM,
params=[Param("value", float, "uL/s",
limits=Range(0, 200, "uL/s"))])
def set_flow(self, value: float): ...
# that's the whole integration. Everything else is derived.
Scaffolded, then verified
labaiagent scaffold acme.p200 emits the driver + test skeleton; labaiagent verify runs a strict conformance suite (halt coverage, limit sanity, read purity) before an agent ever sees it.
No API? Still integrable
The watched-folder transport turns 'vendor software drops a CSV' into a synchronous, audited read — the most common awkward case in an installed lab.
Site-specific limits without forks
Lab YAML narrows this instance's limits (your 80 °C bath vs. the 150 °C one downstairs). Config can only TIGHTEN — a widened limit is refused at startup.
Notes: This is the TCO slide. The whole driver is ~25 lines; the CLI scaffolds it with tests, and `labaiagent verify` runs a strict conformance suite before it ever meets an agent. Instruments with NO API integrate via the watched-folder transport.

## Slide 14
Where it stands — and the pilot that closes the gap
We will not claim what we have not measured. Here is exactly what is proven, what is not, and the 4-week path between them.
LabAIAgent · technical briefing
14
Proven today
Framework, safety engine, gateway, recovery: 232 tests, live-socket HTTP, crash-and-resume proven in CI
Opentrons + SCPI wire contracts verified against fakes speaking the published protocols
4 published adversarial review rounds; every finding fixed + regression-tested
Stated limits (also in writing, in the repo)
Not yet run against physical instruments — the IQ/OQ/PQ exists precisely to close this
A software e-stop is a layer ABOVE hardware E-stops and interlocked enclosures, never a substitute
Part 11 compliance is a property of your validated deployment, not of any software alone
The 4-week pilot
Wk 1
Install + IQ on your workstation; connect 2 instruments (one liquid handler, one reader); --readonly with your agents
Wk 2
OQ: every capability exercised live, out-of-range refusals, e-stop drill, fault injection, kill-and-resume, watchdog unplug
Wk 3
PQ: your real assay ×3, two operators, gravimetric volume check; every run leaves a signed record
Wk 4
Evidence review: executed IQ/OQ/PQ + audit chains + run records = your compliance file, our validation dataset, one shared methods paper
Ask: two instruments, one real assay, four weeks. Everything you need is already in the repo.
Notes: Close on honesty + concrete ask. The pilot produces three artifacts at once: their compliance evidence, our validation dataset, and a co-authorable methods paper. Recommended close: pick two instruments and a real assay.